## Slide 1
Automated Traffic Light
Duration System
Using Computer Vision on NVIDIA Jetson Nano
Aditya Nahata | Roll No: 1024240083 | Group: 2X13
UTA035 – Engineering Design Project (Edge Computing) | TIET, Patiala | April 2026

## Slide 2
PROBLEM
Problem Statement
2 / 10
The Challenge
Fixed-timer traffic lights waste green time on empty lanes
Dense lanes wait too long, causing unnecessary congestion
No real-time adaptation to actual vehicle density
Road-sensor based systems are expensive to install
Our Solution
A camera-based, edge AI system on Jetson Nano that detects vehicles in real time and dynamically adjusts green light duration per lane — no road sensors needed.
❌ Fixed Timer System
Green time: always 30s
Lane A: 2 cars → 28s wasted
Lane B: 20 cars → 30s not enough
✅ Adaptive System (Ours)
Lane A: 2 cars → 14s green
Lane B: 20 cars → 50s green
Result: ~35% less wait time

## Slide 3
OBJECTIVES
Project Objectives
3 / 10
📷
Real-time Detection
Detect and count vehicles in each lane from live camera feed using YOLOv8-nano on Jetson Nano.
⏱
Adaptive Duration
Dynamically compute green light duration based on vehicle density using the adaptive formula.
🚦
Signal Control
Drive the GREEN/YELLOW/RED signal cycle per lane with OpenCV visual overlay output.
⚡
Edge Performance
Achieve real-time FPS on Jetson Nano using TensorRT-optimised inference without cloud.
🔧
Modular Code
Build a clean, well-documented Python codebase with separate modules for detection, control, and display.
📊
Performance Metrics
Evaluate detection accuracy (mAP), processing speed (FPS), and signal timing efficiency.

## Slide 4
METHODOLOGY
Methodology & System Block Diagram
4 / 10
Camera
Input
YOLOv8
Detection
Vehicle
Count/Lane
Adaptive
Algorithm
Signal
Control
Adaptive Formula: green_time = clamp( 10 + count × 2, T_min=10s, T_max=60s )
Detection
Model: YOLOv8-nano
Input: 640×640 px
Classes: car, bike, bus, truck
Conf threshold: 0.4
Control Logic
State: GREEN → YELLOW → RED
Yellow fixed: 3 seconds
Round-robin lane cycling
Real-time count update
Output
OpenCV HUD overlay
Lane signals + timer
Vehicle count per lane
FPS display

## Slide 5
REQUIREMENTS
Hardware & Software Requirements
5 / 10
Hardware
Component | Specification
NVIDIA Jetson Nano | 4GB RAM, 128-core Maxwell GPU
Camera | USB Webcam / CSI Camera v2
CPU | Quad-core ARM Cortex-A57 @ 1.43 GHz
Storage | 32 GB microSD (Class 10)
OS | Ubuntu 18.04 (JetPack 4.6)
Power | 5V 4A via barrel jack
Software Stack
🐍
Python 3.8
Primary language
👁
OpenCV 4.8
Frame capture & display
🤖
YOLOv8 (Ultralytics)
Vehicle detection model
🔥
PyTorch 1.11
Jetson-compatible wheel
⚡
TensorRT 8.2
Inference optimisation
🖥
VS Code + Remote SSH
Development environment

## Slide 6
IMPLEMENTATION
Implementation
6 / 10
Project Structure
traffic_light_project/
├── main.py
├── requirements.txt
├── README.md
├── utils/
│ ├── detector.py
│ ├── traffic_controller.py
│ └── display.py
├── models/
│ └── yolov8n.pt
└── data/
Setup Steps
1
Install JetPack 4.6
Flash SD card, enable CUDA, cuDNN, TensorRT
2
Connect via Remote SSH
VS Code → Remote SSH → Jetson Nano IP → open project folder
3
Install dependencies
pip install ultralytics opencv-python numpy --break-system-packages
4
Run the system
python main.py --source 0 --lanes 2 --conf 0.4

## Slide 7
CODE WALKTHROUGH
Code Screenshots
main.py - Imports & Arguments
main.py - Detection Loop (while True)
main.py - Components Initialization
traffic_controller.py - Adaptive Formula

## Slide 8
ARCHITECTURE
System Architecture
7 / 10
1
Live Camera Feed
USB/CSI camera → OpenCV VideoCapture
2
Frame Preprocessing
Resize 640×640, BGR→RGB, normalise
3
YOLOv8-nano Inference
Vehicle detection, bounding boxes
4
Lane Assignment
cx of bbox → lane index (0 or 1)
5
Adaptive Controller
green_time = 10 + count×2 (clamped)
6
Signal Output
OpenCV HUD + GPIO LEDs (optional)

## Slide 9
LIVE DEMO OUTPUT
Terminal Output — Jetson Nano (Headless)
Inference Analysis
4 vehicles detected
Green time: 18s (vs 10s base)
5 vehicles detected
Lane 0: 16s, Lane 1: 14s
Formula Verified:
10 + 4x2 = 18s
10 + 3x2 = 16s
Platform: Jetson Nano
Headless mode via SSH
YOLOv8n model running live

## Slide 10
RESULTS
Results & Performance
8 / 10
22–30
FPS
With TensorRT
72%
mAP@0.5
Vehicle Detection
~35%
Less Wait
vs Fixed Timer
10–60
Seconds
Adaptive Range
Metric | No TensorRT | With TensorRT
FPS | 10–14 FPS | 22–30 FPS
GPU Memory | ~1.2 GB | ~0.8 GB
CPU Load | ~35% | ~22%
mAP@0.5 | ~72% | ~72%

## Slide 11
CHALLENGES
Challenges, Solutions & Applications
9 / 10
Challenges & Solutions
⚠ PyTorch on Jetson Nano
✓ Used NVIDIA's JetPack-compatible PyTorch wheel
⚠ Low FPS without GPU
✓ Exported model to TensorRT FP16 format
⚠ Night-time detection drop
✓ Tuned confidence threshold to 0.4; add IR option
⚠ Lane boundary without sensors
✓ Virtual lane strips by horizontal pixel division
Real-world Applications
🏙
Smart City Intersections
Adaptive signals at urban junctions without road sensors
🏗
Construction Zones
Temporary adaptive signals at single-lane road works
🚑
Emergency Corridors
Extend green for heavy-traffic routes during incidents
🛣
Highway Ramp Metering
Control on-ramp flow based on real-time vehicle count

## Slide 12
Conclusion & Future Scope
Conclusion
Successfully built a real-time adaptive traffic signal system on Jetson Nano
YOLOv8-nano achieves 22–30 FPS with TensorRT — suitable for live deployment
Green duration adapts dynamically from 10s to 60s based on vehicle density
~35% reduction in average wait time vs fixed-timer baseline
Fully modular Python codebase — easy to extend and maintain
Future Scope
GPIO integration to control physical traffic light LEDs
4-way intersection with multi-camera support
Emergency vehicle detection & priority override
Pedestrian & cyclist phase integration
Multi-intersection corridor-level coordination
Custom YOLO model trained on Indian traffic data
Thank You
Aditya Nahata | 1024240083 | Group 2X13 | UTA035 – EDP (Edge Computing) | TIET Patiala | April 2026
10 / 10